ENGINE COMPANY OPERATIONS

1)  	   	Fast Attack: Handline Div.1

2)  	   	Fast Attack: Handline Div.2

Hose Deployment Standard

- Pull a 200’ pre connected 1 ¾

- Deployment will be performed by one firefighter up until the point that the line enters the structure

- One firefighter will pull the hose and assure that all hose is removed from the hosebed.  The firefighter is expected to be able to accomplish this task without the assistance of the Driver Engineer or Company Officer

- The firefighter will advance the hose to the point of entry

- The firefighter will deploy the hose in an manner that minimizes kinks

- The firefighter will lay out the hose in a way that the hose will not be snagged or obstructed when advanced

- The firefighter will arrive at the point of entry with sufficient hose to reach the fire and with a deployment that will allow for the easiest advancement into the structure

| LFD Standard October 2007 | Under 2:30 Minutes (actual 2:12) |
| --- | --- |

COMPANY EFFICIENCY DRILL #1 REVISED

“FAST ATTACK, Division 1”

TASK:     Crew shall advance and operate a 200’ x 1 ¾” handline at grade level within Division1.

PROCEDURE:

- Evolution will start with personnel in normal riding positions dressed as they would ordinarily respond to a fire.

- SEAT BELTS ARE NOT RELEASED and DOORS ARE NOT OPENED UNTIL TIME STARTS.

- The apparatus shall set within a designated area.

- The Driver / Engineer will ensure that the wheels are chocked.

- The Driver / Engineer shall have the appropriate level of PPE.

- The Firefighter in full bunker gear and wearing SCBA &  “ON AIR WHEN WATER IS FLOWING” shall stretch and operate one 200’ x 1 ¾” pre-connect handline at the doorway of Division 1.

- The line shall be stretched to the Division 1 doorway.

- The Company Officer shall back up the firefighter on the line and on air.

- The Driver / Engineer shall charge the line and pump the appropriate pressure.

TIMING:

- Time will start on go.

- Time will stop when handline is at fully advanced, Officer and Firefighter are at the nozzle and “ON AIR”, and water is discharged from the nozzle at proper flow & pressure.

| LFD Standard October 2007 | Under 3 Minutes (actual 2:59) |
| --- | --- |

COMPANY EFFICIENCY DRILL #2

“FAST ATTACK, Division 2”

TASK:  Crew shall advance and operate a 200’ x 1 ¾” handline up a stairway to the second floor (Division 2) of a building, stretch horizontally

through a room, & discharge water out an open window.

PROCEDURE:

- Evolution will start with personnel in normal riding positions and dressed

as they ordinarily would respond to a fire.

- SEAT BELTS ARE NOT RELEASED and DOORS ARE NOT OPENED

UNTIL TIME STARTS.

- The apparatus shall be set within a designated area.

- The Driver / Engineer will ensure that the

wheels are chocked.

- The Driver / Engineer shall have the appropriate level of PPE.

- The Officer and Firefighter in full bunker gear and wearing SCBA & “ON

AIR WHEN WATER IS FLOWING”, shall stretch one 200’ 1 ¾” preconnect handline to the second floor of a designated building.

- The line shall be advanced up an interior stairway to the second floor

landing where the Officer shall order the line to be charged.

- The charged line will then be advanced and operated out an open second

floor window.

- The Driver / Engineer shall charge the line and pump the appropriate

pressure.

TIMING:

- Time will start on go.

- Time will stop when the Officer and Firefighter are at the nozzle, with

water flowing, and nozzle visible at the designated window on Division 2.